## Slide 1: Jacobian – Implications & Applications
Singularity & Performance & Design
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 2: Jacobian Methods – Reference Frame - Summary
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 3: Jacobian Methods of Derivation & the Corresponding Reference Frame – Summary
Method | Jacobian Matrix Reference Frame | Transformation to Base Frame (Frame 0)
Explicit (Diff. the Forward Kinematic Eq.) |  | None
Iterative Velocity Eq. |  | Transform Method 1: Transform Method 2:
Iterative Force Eq. |  | Transpose Transform
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 4: Propagation to the Tip of the Tool
Problem Defenition
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 5: Propagation to the Tip of the Tool – Problem Definition
Problem
  Practical Configuration of a robotic arm - The robotic arm typically includes the following
    F/T Sensor
    Gripper / End Effector
    Tool
  Analysis – The generic analysis of the robotic arm mapping position, velocities and forces / torques between the base and the wrist (last frame of the manipulators)
  Rational –
    Generic Analysis versus task specific elements (F/T sensor, gripper tool) - The analysis is conducted by the robot arm manufacturer however the F/T sensor, the gripper and the tool are task specific and selected by the user.
    Tool Change – The same arm performing different tasks may need different tools that are changed during the course of its operation
  Need – The need is typically to
    Trace the position and orientation and velocities (linear and angular) of the tool tip as it follows a trajectory
    Express force and torques applied on the environment by the tool tip and vice versa by a force sensor measuring these parameters in a different location
Solution – Expressing position, velocity forces and torques from the last frame (Frame 6 at the wrist) to the tip of the tool
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 6: Propagation to the Tip of the Tool
Position
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 7: Jacobian Propagation to the Tip of the Tool – Position
In a case where the tool tips follows a trajectory, the path defines the goal position and orientation
Since the tool is attached to the end effector its position does not change as a function of time with respect to frame 6
Multiply both sides of the equations by
Solve the Inverse Kinematics
Known
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 8: Jacobian Propagation to the Tip of the Tool
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 9: Jacobian Propagation to the Tip of the Tool
Forces/Torques
Velocities (Linear and Angular)
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 10: Jacobian Propagation to the Tip of the Tool
Velocity
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 11: Jacobian Propagation to the Tip of the Tool – Position
Position
Matrix Form
Vector Form
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 12: Jacobian Propagation to the Tip of the Tool - Velocities
Velocity of two rigidly connected frames (rigid body)
Vector Form
Matrix Form
Note: The equations are formulated as a forward propagation i.e propagating from frame {i} to {i+1}. Challenge: We know the linear and angular velocities at the tip of the tool i.e. frame {T} and we wish to express the velocities by backwards propagation to the wrist i.e. frame {6} or frame {w}
Solution: Find the expressions for as a function of
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
0 (Rigid)

## Slide 13: Jacobian Propagation to the Tip of the Tool - Velocities
Expressing the equations in a back propagation fashion given the linear and angular velocities in frame {i} or frame {w} as a function of the linear and angular velocities in frame {i+1} or frame {T}
Finding expressions for and Multiply both sides of the equation by
Resulting in vector form
and a matrix form
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 14: Jacobian Propagation to the Tip of the Tool – Velocities - Summary
Preform the following replacement of indexes
Resulting in vector form
and a matrix form
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 15: Jacobian Propagation to the Tip of the Tool – Forces/Torques
Force and torque applied on a rigid body
Vector Form
Matrix Form
Note: The equations are formulated as a backward propagation i.e propagating from frame {i+1} to {i}. Challenge: The Force/Torque (F/T) sensor i.e. frame {S} is located between the tool tip i.e. frame {T} and the wrist i.e. frame {6} or frame {w}
Solution: Find an expression for the forces and torque applied on the tool tip but measured by the sensor
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 16: Jacobian Propagation to the Tip of the Tool
The end effector holds a tool on which forces and torques are applied
A force/torque sensor is attached close to the wrist that is expected to measure the forces and torque applied on the tool
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 17: Jacobian – Singularity Problem Definition
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 18: Inverse Jacobian
Given
  Tool tip path (defined mathematically)
  Tool tip position/orientation
  Tool tip velocity
  Jacobian Matrix
Problem: Calculate the joint velocities
Solution:
  Compute the inverse Jacobian matrix
  Use the following equation to compute the joint velocity
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 19: Singularity - The Concept
Motivation: We would like the hand of a robot (end effecror) to move with a certain velocity vector in Cartesian space. Using linear transformation relating the joint velocity to the Cartesian velocity we could calculate the necessary joint rates at each instance along the path.
Given: a linear transformation relating the joint velocity to the Cartesian velocity (usually the end effector)
Questions:
  Is the Jacobian matrix invertible? (Or) Is it nonsingular?
  Is the Jacobian invertible for all values of ?
  If not, where is it not invertible?
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 20: Inverse Jacobian
Cases in which the Jacobian matrix is not inevitable ( does not exists).
Non invertible matrix is called singular matrix
  Case 1 - The Jacobian matrix is not squared
  In general the 6xN Jacobian matrix may be non-square in which case the inverse is not defined
  Case 2 - The determinant is equal to zero
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 21: Singularity - The Concept
Answer (Conceptual): Most manipulator have values of where the Jacobian becomes singular . Such locations are called singularities of the mechanism or singularities for short
Singularities of the mechanism
Workspace interior Singularities
Workspace boundary singularities
End
Effector
Workspace
Boundary
- Stretched out
- Folded back
- Two or more joints are lining up
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 22: Singularity - The Concept
Lost of DOF - Losing one or more DOF means that there is a some direction (or subspace) in Cartesian space along which it is impossible to move the hand of the robot (end effector) no matter which joint rate are selected
Load Balance – A finite force can be applied to the end effector that produces no torque at the robot’s joints
Joint Velocity – A zero end effector velocity will cause high joint velocity
Manipulator
Singular
Configuration
Losing
One or More DOF
General
Configuration
All DOF
Are Available
Problematic
Load Balance
Problematic
Joint Velocity
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 23: Singularity – Physical Interpretation - Examples
Type of Singularities
  Wrist
  Elbow
  Shoulder
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 24: Singularity – Physical Interpretation - Examples
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 25
Singularities

## Slide 26
Singularities

## Slide 27
Singularities

## Slide 28: Jacobian – Singularity Example 1 – 2R Elbow Singularity Singularity at the Edge of the Workspace
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 29: Jacobian Matrix by Differanciation - 3R - 1/4
Consider the following 3 DOF Planar manipulator
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 30: Jacobian Matrix by Differanciation - 3R - 4/4
Using a matrix form we get
The Jacobian provides a linear transformation, giving a velocity map and a force map for a robot manipulator. For the simple example above, the equations are trivial, but can easily become more complicated with robots that have additional degrees a freedom. Before tackling these problems, consider this brief review of linear algebra.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 31: Properties of the Jacobian - Velocity Mapping and Singularities
Example: Planar 3R
Note that is not a function of
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 32: Properties of the Jacobian - Velocity Mapping and Singularities
The manipulator loses 1 DOF. The end effector can only move along the tangent direction of the arm. Motion along the radial direction is not possible.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 33: Properties of the Jacobian - Force Mapping and Singularities
The relationship between joint torque and end effector force and moments is given by:
The rank of is equals the rank of
At a singular configuration there exists a non trivial force such that
In other words, a finite force can be applied to the end effector that produces no torque at the robot’s joints. In the singular configuration, the manipulator can “lock up.”
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 34: Properties of the Jacobian - Force Mapping and Singularities
Example: Planar 3R
In this case the force acting on the end effector (relative to the {0} frame) is given by
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 35: Properties of the Jacobian - Force Mapping and Singularities
For we get
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 36: Jacobian – Singularity Example 2 – 3R Shoulder Singulaity Singularity Inside the Workspace
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 38: Jacobian: Singular Configuration - 3R Example
If we want to use the inverse Jacobian to compute the joint angular velocities we need to first find out at what points the inverse exists.
Considering the 3R robot
The determinate of the Jacobian is defined as follows
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 39: Jacobian: Singular Configuration - 3R Example
The reduced Jacbian matrix is singular when it determinate is equal to zero
The singular condition occur when either of the following are true
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 40: Jacobian: Singular Configuration - 3R Example
Case 1:
The first row of the Jacobian is zero
The 3R robot is loosing one DOF.
The robot can no longer move along the X-axis of frame {4}
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 41: Jacobian: Singular Configuration - 3R Example
Case 2:
Occur only if
The third row of the Jacobian is zero
The origin of frame {4} intersects the Z-axis of frame {1}
The 3R robot is loosing one DOF.
The robot can no longer move along the Z-axis of frame {4}
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 42: Joint Velocity Near Singular Position - 3R Example
Robot : 3R robot
Task: Visual inspection
Control
Control
Robot
Operator
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 43: Joint Velocity Near Singular Position - 3R Example
Singularity (Case 2)- The origin of frame {4} intersects the Z-axis of frame {1}
Solve for in terms of we find
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 44: Joint Velocity Near Singular Position - 3R Example
Singularity -
Problems:
  Motor Constrains - The robot is physically limited from moving in unusual high joint velocities by motor power constrains. Therefore, the robot will be unable to track the required joint velocity trajectory exactly resulting in some perturbation to the commanded Cartesian velocity trajectory.
  Gears and Shafts - The derivative of the angular velocity is the angular acceleration. The high acceleration of the joint resulting form approaching too close to a singularity may cause damage to the gear/shafts.
  DOF - At a singular configuration (specific point in space) the manipulator loses one or more DOF.
Consequences – Certain tasks can not be performed at a singular configuration
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 45: Jacobian – Singularity Example 3 – 3R Wrist Singularity Singularity Inside the Workspace
Instructor: Jacob Rosen
Advanced Robotic - MAE 263B - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 46: Mapping - Rotated Frames - Z-Y-Z Euler Angles
Start with frame {4}.
Rotate frame {4} about by an angle
Rotate frame {4} about by an angle
Rotate frame {4} about by an angle
Note - Each rotation is preformed about an axis of the moving reference frame, rather then a fixed reference.
Euler Angles
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 47: Mapping - Rotated Frames - Z-Y-Z Euler Angles
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 48: Mapping - Rotated Frames - Z-Y-Z Euler Angles
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 49: Mapping - Rotated Frames - Z-Y-Z Euler Angles
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 50: Three consecutive Axes Intersect - wrist
Goal
Direct Kinematics
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 51: Three consecutive Axes Intersect - wrist
Solve for
using element
Using the Atan2 function, we find
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 52: Three consecutive Axes Intersect - wrist
Solve for using elements

## Slide 53: Three consecutive Axes Intersect - wrist
Solve for using elements
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 54: Three consecutive Axes Intersect - wrist
Note: Two answers exist for angle which will result in two answers each for angles and
If the solution degenerates
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 55: Three consecutive Axes Intersect - wrist
We are left with for every case. This means we can’t solve for either, just their sum.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 56: Three consecutive Axes Intersect - wrist
One possible convention is to choose
The solution can be calculated to be
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 57: Three consecutive Axes Intersect - wrist
For this example, the singular case results in the capability for self-rotation. That is, the middle link can rotate while the end effector’s orientation never changes.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 58: Gimbal Lock
Normal situation
The three gimbals are independent
Gimbal lock:
Two out of the three gimbals are in the
same plane, one degree of freedom is lost
http://youtu.be/zc8b2Jo7mno
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 59: Gimbal Lock – Robotics
In robotics, gimbal lock is commonly referred to as "wrist flip", due to the use of a "triple-roll wrist" in robotic arms, where three axes of the wrist, controlling yaw, pitch, and roll, all pass through a common point.
An example of a wrist flip, also called a wrist singularity, is when the path through which the robot is traveling causes the first and third axes of the robot's wrist to line up. The second wrist axis then attempts to spin 180° in zero time to maintain the orientation of the end effector. The result of a singularity can be quite dramatic and can have adverse effects on the robot arm, the end effector, and the process.
The importance of non-singularities in robotics has led the American National Standard for Industrial Robots and Robot Systems — Safety Requirements to define it as "a condition caused by the collinear alignment of two or more robot axes resulting in unpredictable robot motion and velocities".
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 60: Properties of the Jacobian - Force Mapping and Singularities
This situation is an old and famous one in mechanical engineering.
For example, in the steam locomotive, “top dead center” refers to the following condition
The piston force, F, cannot generate any torque around the drive wheel axis because the linkage is singular in the position shown.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 61: Properties of the Jacobian - Velocity Mapping and Singularities
We have shown the relationship between joint space velocity and end effector velocity, given by
It is interesting to determine the inverse of this relationship, namely
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 62: Properties of the Jacobian - Velocity Mapping and Singularities
Consider the square 6x6 case for .
If rank < 6 ( ) , then there is no solution to the inverse equation (see Brief Linear Algebra Review - 1,7).
However, if the rank = 5, then there is at least one non-trivial solution to the forward equation (see Brief Linear Algebra Review - 7). That is, for
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 63: Properties of the Jacobian - Velocity Mapping and Singularities
The solution is a direction in the in joint velocity space for which joint motion produces no end effector motion.
We call any joint configuration for which
a singular configuration.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 64: Properties of the Jacobian - Velocity Mapping and Singularities
For certain directions of end effector motion ,
where:
  are the eigenvalues of
  are the eigenvectors of
If is fully ranked (see Brief Linear Algebra Review - 6/ ), we have
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 65: Properties of the Jacobian - Velocity Mapping and Singularities
As the joint approach a singular configuration there is at least one eigenvalue for which . This results in
In other word, as the joints approach the singular configuration, the end effector motion in a particular task direction causes the joint velocities to approach infinity. However, there are task velocities that can have solutions.
If loses rank by only one, then there are n-1 eigenvectors in the task velocity space ( ) for which solutions do exist. However, there can be multiple solutions.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 66: Physical Expressions of Singularity – Summary
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 67: Physical Expressions of Singularity
DOF
  Phenomena -
  Kinematic Deficiency –
  Mechanical Risk -
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Shoulder
Elbow
Wrist

## Slide 68: Physical Expressions of Singularity
DOF
  Phenomena - Losing one or more DOF
  Kinematic Deficiency – Inability to move in a specific direction
  Mechanical Risk - None
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Shoulder
Elbow
Wrist

## Slide 69: Physical Expressions of Singularity
Velocity
  Phenomena -
  Kinematic Deficiency –
  Mechanical Risk -
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Shoulder
Elbow
Wrist

## Slide 70: Physical Expressions of Singularity
Velocity
  Phenomena - High velocities (theoretically infinity) of some joints, and zero velocities in other directions
  Kinematic Deficiency – Inability to provide the required joint velocity to support the end effector velocity
  Mechanical Risk - High demand of joint velocities may damage the actuator/gear/joint
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Shoulder
Elbow
Wrist

## Slide 71: Physical Expressions of Singularity
Forces / Torques
  Phenomena -
  Kinematic Deficiency –
  Mechanical Risk -
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Shoulder
Elbow
Wrist

## Slide 72: Physical Expressions of Singularity
Forces / Torques
  Phenomena - High external loads applied on the end effector resulted with zero joint torques generated at the joint.
  Kinematic Deficiency - None
  Mechanical Risk - The high loads deform the links and can potential damage them
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Shoulder
Elbow
Wrist

## Slide 73: Jacobian – Duality
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 74: Jacobian – Duality
is a linear mapping of the joint space velocities which is a n - dimensional vector space to the end effector velocities which is a m – dimensional vector space
Joint Space
End-Effector Space
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 75: Jacobian – Duality
The subset of all the end effector velocities resulting from the mapping represents all the possible end effector velocities that can be generated by the n joints given the arm configuration
Joint Space
End-Effector Space
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 76: Jacobian – Duality
If the rank of the Jacobian matrix is at full of row rank (square matrix) the joint space
covers the entire end effector vector otherwise there is at least one direction in which the end effector can not be moved
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 77: Jacobian – Duality
The subset is the null space of the linear mapping. Any element in this subspace is mapped into a zero vector in such that therefore any joint velocity vector that belongs to the null space does not produce any velocity at the end effector
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 78: Jacobian – Duality
If the Jacobian of a manipulator is full rank the dimension of the null space is the same as the redundant degrees of freedom (n-m). For example the human arm has 7 DOF whereas the hand may have 6 linear and angular velocities therefore the null dimension is one (n-m=7-1=1)
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 79: Jacobian – Duality
If the Jacobian of a manipulator is full rank (i.e. n>m full row rank where the rows are linearly independent) the dimension of the null space is the same as the redundant degrees of freedom (n-m). For example the human arm has 7 DOF whereas the hand may have 6 linear and angular velocities therefore the null dimension is one (n-m=7-1=1)
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 80: Jacobian – Duality
If the Jacobian of a manipulator is full rank (i.e. for redundant manipulator n>m full row rank where the rows are linearly independent) the dimension of the null space is the same as the redundant degrees of freedom (n-m). For example the human arm has 7 DOF whereas the end effector (hand) may have 6 linear and angular velocities therefore the null dimension is one (n-m=7-1=1)
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 81: Jacobian – Duality
When the Jacobian matrix degenerates (i.e. not full rank e.g. due to singularity) the dimension of the range space decreases at the same time as the dimension of the
null space increases by the same amount. The sum of the two is always equal to n
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 82: Jacobian – Duality
If the null space is not empty set, the instantaneous kinematic equation has an infinite number of solutions that cause the same end effector velocities (recall the 3 axis end effector)
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 83: Jacobian – Duality
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Accessible
None Accessible
Unlike the mapping of the instantaneous kinematics the mapping of the static external forces is from the m-th vector space associated with the end effector coordinates to the n-th dimensional vector space associated with the torques at the joint space. Therefore the joint torque are always determined uniquely from any end effector point force
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 84: Jacobian – Duality
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Accessible
None Accessible
The null space represents the set of all end point forces that do not require any torques at the joints to bear the corresponding load (e.g. 2R fully stretched or collapsed elbow).
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 85: Jacobian – Duality
Joint Space
End-Effector Space
In at least on direction
Accessible
None Accessible
Accessible
None Accessible
When the Jacobian matrix is degenerated or the arm is in a singular configuration external endpoint force is borne entirely by the structure and not by the joint torque.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA