## Slide 1: Jacobian – Implications & Applications Part 2: Design - Manipulability Ellipsoid & Performance Index
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 2: Performance Index – Manipulability
Kinematic Singularity – The robot end effector loses its ability to translate or rotate in one or more directions
Kinematic Singularity – Binary - A kinematic singularity presents a binary proposition – a particular configuration is either kinematically singular or it is not
Proximity to Singularity - it is reasonable to ask if a nonsingular configuration is “close” to being singular.
Manipulability Ellipsoid - The manipulability ellipsoid allows one to visualize geometrically the directions in which the end-effector moves with least effort or with greatest effort
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 3: Jacobian – Singularity – Mathematical Introduction
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Robotic
System
Non Singular
Conditions
Singular
Conditions

## Slide 4: Jacobian – Singularity – Mathematical Introduction
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 5: Jacobian – Singularity – Mathematical Introduction
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
General expression of the end effector velocity ellipsoid

## Slide 6: Jacobian – Singularity – Mathematical Introduction
Linear Algebra – Norm – Definition
  Norm P - norm of x
  Calculate the absolute value of the i-th element
  take its power p
  sum all these power absolute values
  take the power of the result
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 7: Jacobian – Singularity – Mathematical Introduction
  Norm P=0 - norm of x
    Using the power of 0 with an absolute values will get you
      1 for every non-zero value
      0 for every zero value
    This norm corresponds to the number of non-zero elements in the vector
  Norm P=1 - norm of x
    The sum of the absolute values
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 8: Jacobian – Singularity – Mathematical Introduction
  Norm P=2 - norm X (Euclidean Norm)
    The absolute value is not needed anymore since x is squared
    Provide the length of the vector in Pythagorean theorem
    Example
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 9: Jacobian – Singularity – Mathematical Introduction
  - Squared Euclidean norm (Squared norm)
    Alternative expressions for
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 10: Jacobian – Singularity – Mathematical Introduction
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 11: Jacobian – Singularity – Mathematical Introduction
A circle/sphere of joint velocities, like the circle shown here is defined by the equation
Using the definition of the Jacobian
Assume that the Jacobian is invertible (not strictly necessary) the previous equation can be rewritten as
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 12: Jacobian – Singularity – Mathematical Introduction
Based on Linear Algebra property
The previous equations
Can be rewritten as
Based on linear Algebra properties
The previous equation can be rewritten as
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 13: Jacobian – Singularity – Mathematical Introduction
Rewriting
where
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
properties:
– is positive
– symmetric

## Slide 14: Performance Index – Manipulability
Performing eigenvector/eigenvalue analysis of defining
  Eigenvectors
  eigenvalues
The directions of the principal axes of the ellipsoid are and the lengths of the principal semi-axes are
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 15: Jacobian – Singularity – Mathematical Introduction
Replace (velocity of the tip) by a vector x
(symmetric, positive definite)
The A matrix defines an ellipsoid of x values that satisfy the equation
If
Then Manipulability Ellipsoid Resulting from a unit sphere of joint velocity
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Eigenvalues of A
Eigenvectors of A

## Slide 16: Jacobian – Singularity – Mathematical Introduction
If
Then Manipulability Ellipsoid Resulting from a unit sphere of joint velocity
If
Then Force Ellipsoid Resulting from a unit sphere of joint forces or torques
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 17: Performance Index – Manipulability
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Joint Space
Joint Space
Task Space
Task Space

## Slide 18: Jacobian – Singularity – Mathematical Introduction
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
  Same principle axes
  Same semi axis lengths
  Small velocity can be applied in direction of large forces
  Small forces can be applied in direction of large velocities
Force ellipsoid
Manipulability ellipsoid

## Slide 19: Jacobian – Singularity – Mathematical Introduction
  Assigning a single number representing how close the robot is to being a singular
  OR
  Reducing the representation of the ellipsoid into a single number
  Performance Index
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 20: Performance Indices
Definition
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 21: Performance Index Measure No.1 - Isotropy
Isotropy – The ratio of the longest and shortest semi-axes of the manipulability ellipsoid
  When then the manipulability ellipsoid is nearly spherical or isotropic, meaning that it is equally easy to move in any direction. This situation is generally desirable
  When the robot approaches a singularity
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 22: Performance Index Measure No.2 – Condition Number
Manipulability Measure No. 2 – Condition Number – Squaring the isotropy measure
  When then the manipulability ellipsoid is nearly spherical or isotropic, meaning that it is equally easy to move in any direction. This situation is generally desirable
  When the robot approaches a singularity
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 23: Performance Index – Manipulability
Manipulability Measure No. 3 – Manipulability – The volume V of the ellipsoid is proportional to the product of the semi-axis lengths
The Manipulability is defined as
  A good manipulator design has large area of characterized by high value of the manipulability
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 24: Performance Index – Manipulability
Given the structure of the Jacobian matrix, it makes sense to separate it into the two sub matrixes because the units of
  are linear velocities (m/s) and the unites of
  are angular velocities (rad/s)
This leads to two three-dimensional manipulability ellipsoids, one for linear velocities and one for angular velocities.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
Linear velocity/force ellipsoids
Angular velocity/moment ellipsoids

## Slide 25: Performance Index – Manipulability
When calculating the linear-velocity manipulability ellipsoid ( ),
it generally makes more sense to use the Jacobian expressed in the end effector space
instead of the Base Frame
since we are usually interested in the linear velocity of the end effector in its own coordinate system than a fixed frame at the base
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 26: Designing Well Conditioned Workspace – Rational
Challenge
  Difficulty in operating at
    Workspace Boundaries
    Neighborhood of singular point inside the workspace
Goal
  Singularity - The further the manipulator is away from singularities the better it moves uniformly and apply forces in all directions
Performance Criterion
  It is useful to assign a single scalar measure defining how easily the robot can move at a given posture.
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 27: Recap
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 28: Performance Index – Manipulability
Manipulabity Ellipsoid - For a general n-joint serial (open chain) and a task space with coordinates the manipulability ellipsoid corresponds to the end-effector velocities for joint rates
satisfying the norm of to be equal to 1
representing a unite sphere in the n-th dimensional joint velocity space
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 29: Performance Index – Manipulability
Assuming J is invertible, the unit joint-velocity condition can be written
If J is full rank the matrix and are
  square,
  symmetric
  positive definite
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 30: Performance Index – Manipulability
For any symmetric positive-definite , the set of vectors satisfying
defines an ellipsoid in the m-dimensional space.
Recap
Represent an circle / sphere
Represent a ellipse / ellipsoid
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 31: Performance Indices - Design
Optimization Approach
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 32: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 33: Jacobian – Design - Performance Index – Optimization – Pseudo Code
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
FOR
FOR
Check if the link lengths allows the tip to reach all the points in
the workspace by solving the IK for every point in the workspace
IF NOT select a new pair of
FOR
FOR
[Calculate the angles using IK]
[Calculate and ]
[Calculate the eigenvalues of ]
[Calculate ]
[Populate ]
END (FOR )
END (FOR )
[Calculate ]
[Calculate ]
[Calculate ]
[Calculate optimal ]
END (FOR )
END (FOR )
[Select max ]

## Slide 34: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 35: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 36: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 37: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 38: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 39: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
FOR
FOR
Check if the link lengths allows the tip to reach all the points in the workspace by solving the IK for every point in the workspace
IF
IF
    FOR
    FOR
    [Calculate the angles using IK]

## Slide 40: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 41: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
[Calculate and ]
[Calculate the eigenvalues of ]
[Calculate ]
[Populate ]
END (FOR )
END (FOR )

## Slide 42: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 43: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
[Calculate ]
[Calculate ]
[Calculate ]
[Calculate optimal ]
END (OF )
END (OF )

## Slide 44: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 45: Jacobian – Design - Performance Index – Optimization
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA
- Search for MAX in OPT
- Find

## Slide 46: Design – Example
Instructor: Jacob Rosen
Advanced Robotic - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 47: RAVEN – A SURGICAL ROBTICS SYSTEM DESIGN – Specifications
Notes: 47

## Slide 48
Notes: 48

## Slide 51: Blue DRAGON
Notes: This video clip shows the synthesized haptic and visual interface while performing one of the tool tissue interaction called grasping-pushing-sweeping

## Slide 52: Engineering Specifications - BlueDRAGON
Notes: 52

## Slide 53: Kinematic Analysis – Playback Simulation using Measured Data

## Slide 54: Robot Optimization - Workspace
Dexterous Workspace (DWS)
  High dexterity region defined by a right circular cone with a vertex angel of 60º
  Contains 95% of the tool motions based on in-vivo measurements.
60o- 60o
Notes: 54

## Slide 55
Notes: 55

## Slide 56
Notes: 56

## Slide 57: Spherical Mechanism - Robot Optimization
Notes: 57

## Slide 58: Optimization of Raven IV – Problem & Parameters (7) Definitions
Notes: Link length
Port placement
Base orientation
Min Isotropy performance

## Slide 59
Notes: 59

## Slide 60: RAVEN – A SURGICAL ROBTICS SYSTEM DESIGN – Kinematic Analysis & Optimization
Notes: 60

## Slide 61: Direct Kinematics – Coordinate Systems Assignment
Notes: 61

## Slide 62: Direct Kinematics – Coordinate Systems Assignment

## Slide 63: Direct Kinematics: DH Parameters - Left and Right Robot
Notes: 63

## Slide 64: Direct Kinematics: Transform Matrix for Left Robot
Notes: 64

## Slide 65: Direct Kinematics: Transform Matrix for Right Robot
Notes: 65

## Slide 66: Direct Kinematics: Solution
Notes: 66

## Slide 67: Inverse Kinematics
6 DOFs for positioning and orienting  Inverse Kinematics
1 DOF for the opening and closing of the grasper  Redundancy
Joint Limit Range

## Slide 68: Inverse Kinematics: Homogeneous Transformation Matrix and Its Inverse
Homogenous Transform Matrix  Inverse
For the left robot,
For the right robot,
Define
Which gives

## Slide 69: Inverse Kinematics
For the left robot,
For the right robot,

## Slide 70: Inverse Kinematics
Four Possible Solutions of
For the left robot,
Resolve
For the right robot,
Resolve

## Slide 71: Inverse Kinematics
With resolved , and
Where
Resolve
Define
We have
According to [1]

## Slide 72: Inverse Kinematics
With resolved , , , and
Where
Check to select between the two solution of
For the left robot,
For the right robot,
For the left robot,
For the right robot,

## Slide 73: Jacobian & Isotropy
The mechanism isotropy is determined by the eigen-values of Jacobian matrix, which can be derived by velocity propagation
General equations for velocity propagation:
For the angular velocity,
For the linear velocity,
For the revolute joint,
For the prismatic joint,

## Slide 74: Jacobian & Isotropy
Initial Condition
Rotation Matrices , which leads to
Link 1 is rotating at about :
For the left robot
For the right robot
Link 2 is rotating at about
Link 3 is frozen with
Translation in homogeneous transformation matrix:
Link 4 is translating at along

## Slide 75: Jacobian & Isotropy
Angular velocity propagation
Linear velocity propagation

## Slide 76: Jacobian & Isotropy
Hence, the velocity of the end-point of Link 3 is with reference to Frame 3 is
Angular Velocity
Linear Velocity
For the right robot
For the left robot
For both the left robot and right robot

## Slide 77: Jacobian & Isotropy
Hence, the Jacobian Matrix is
The mechanism isotropy only depends on the 2X2 sub-matrix to the left corner
For the left robot
For the right robot

## Slide 78: Mechanism Isotropy
Mechanism isotropy - the end-effector's ability of moving in all direction given a specific manipulator configuration.
Definition
Range

## Slide 79: Jacobian & Isotropy
The eigen-values of the Jacobian matrix can be found by solving
Which gives
Define

## Slide 80
Notes: 80

## Slide 81: Optimization of Raven IV – Problem & Parameters (7) Definitions
Notes: Link length
Port placement
Base orientation
Min Isotropy performance

## Slide 82: Optimization of Raven IV – Cost Function
Cost Function
  Geometry - Largest circular common workspace (Area Circumference Ratio)
  Manipulations - Best Isotropy
    Across the common workspace
    Worst case value (min/max problem)
  Mechanics - Stiff mechanism (Smallest Mechanism)
Method
  Brute force search across all the free parameters
Notes: The parameters are …
Maximize area-circumference ratio = optimal size and shape of the common workspace
Sum Iso = maximize the overall isotropy of the common workspace
Iso = maximize the min iso performance
Alpha & beta = minimize the mechanism structure

## Slide 83: Common Workspace – Reference Plane

## Slide 84: Area-Circumference Ratio
Definition
According to the Isoperimetric Inequality, a circle has the largest possible area among all the figures with the length of boundary

## Slide 85: Effect of Limiting Minimum Isotropy Performance

## Slide 86: Optimization of Raven IV surgical System Effect of Limiting Minimum Isotropy Performance
Workspace propagation – Minimum Mechanism Isotropy = 0.2

## Slide 87: Optimization of Raven IV surgical System Overall simulation result
Parameter ranges, resolutions and optimal values
Notes: Range
Resolution
Optimal value

## Slide 88: Optimization of Raven IV - Conclusion