## Slide 1: Manipulator Dynamics 2
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 2: Forward Dynamics
Problem
Given: Joint torques and links
geometry, mass, inertia,
friction, joint torques
Compute: Angular acceleration of the
links (solve differential
equations)
Solution
solve a set of differential equations
Dynamic Equations - Newton-Euler method or Lagrangian Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 3: Inverse Dynamics
Problem
Given: Angular acceleration, velocity and
angels of the links in addition to
the links geometry, mass, inertia,
friction
Compute: Joint torques
Solution
Solve a set of algebraic equations
Dynamic Equations - Newton-Euler method or Lagrangian Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 4: Iterative Newton Euler Equations Steps of the Algorithm
(1) Outward Iterations
  Starting With velocities and accelerations of the base
  Calculate velocities accelerations, along with forces and torques (at the CM)
(2) Inward Iteration
  Starting with forces and torques (at the CM)
  Calculate forces and torques at the joints
Instructor: Jacob Rosen
Advanced Robotic - MAE 263B - Department of Mechanical & Aerospace Engineering - UCLA
)

## Slide 5: Iterative Newton-Euler Equations - Solution Procedure Phase 1: Outward Iteration
Calculate the link velocities and accelerations iteratively from the robot’s base to the end effector
Calculate the force and torques applied on the CM of each link using the Newton and Euler equations
Instructor: Jacob Rosen
Advanced Robotic - MAE 263B - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 6: Iterative Newton-Euler Equations - Solution Procedure Phase 2: Inward Iteration
Use the forces and torques generated at the joints starting with forces and torques generating by interacting with the environment (that is, tools, work stations, parts etc.) at the end effector all the way the robot’s base.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263B - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 7: Manipulator Dynamics – Newton Euler Equations
  The Inertia Tensor (Moment of Inertia)
Instructor: Jacob Rosen
Advanced Robotic - MAE 263B - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 8: Dynamics - Newton-Euler Equations
To solve the Newton and Euler equations, we’ll need to develop mathematical terms for:
  - The linear acceleration of the center of mass
  - The angular acceleration
  - The Inertia tensor (moment of inertia)
- The sum of all the forces applied on the center of mass
- The sum of all the moments applied on the center of mass
Instructor: Jacob Rosen
Advanced Robotic - MAE 263B - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 9: Moment of Inertia – Intuitive Understanding
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 10: Moment of Inertia – Intuitive Understanding
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 11: Moment of Inertia – Intuitive Understanding
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 12: Moment of Inertia – Intuitive Understanding
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 13: Moment of Inertia – Intuitive Understanding
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 14: Moment of Inertia – Intuitive Understanding
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 15: Moment of Inertia – Intuitive Understanding
https://www.youtube.com/watch?v=9SaShn8OkJI
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 16: Moment of Inertia – Intuitive Understanding
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 17: Moment of Inertia – Particle – WRT Axis
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 18: Moment of Inertia – Solid – WRT Axis
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 19: Moment of Inertia – Solid – WRT Coordinate Frame
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 20: Moment of Inertia – Solid – WRT an Arbitrary Axis
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
=

## Slide 21: Moment of Inertia – Solid – WRT an Arbitrary Axis
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 22: Inertia Tensor – WRT a Coordinate Frame at the CM
Expression of the angular momentum of a system of particles about the center of mass, the angular momentum is defined as
Where, is the position vector relative to the center of mass, is the velocity relative to the center of mass.
For a 3D continuum mass of a rigid body, the summation can be replaced by an integration over the entire mass.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 23: Inertia Tensor – WRT a Coordinate Frame at the CM
For a 3D rigid body, the distance between infinitesimal mass and the center of mass G remains constant, and the infinitesimal mass velocity , relative to the center of mass G, due to the rotation of the rigid body by an angular velocity is expressed by
Using the vector identity
the expression the angular momentum is rewritten as
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 24: Inertia Tensor – WRT a Coordinate Frame at the CM
For a 2D rigid body, rotating in its own plane the distance between infinitesimal mass is perpendicular to the angular velocity , therefore the term is zero, as a result the angular velocity vector is parallel to the angular momentum
In the three-dimensional case however, this simplification does not occur, and as a consequence, the angular velocity vector, , and the angular momentum vector, , are in general, not parallel.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
0

## Slide 25: Inertia Tensor – WRT a Coordinate Frame at the CM
In cartesian coordinates, the distance between infinitesimal mass and the center of mass G and the angular velocity vector, are defined as
The expression for the the angular momentum can be expended to
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 26: Inertia Tensor – WRT a Coordinate Frame at the CM
The quantities , , and are called the mass moments of inertia with respect to the x, y and z axis, respectively, and are given by
We observe that the quantity in the integrand is precisely the square of the distance to the x, y and z axis, respectively.
It is also clear, from their expressions, that the moments of inertia are always positive
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 27: Inertia Tensor – WRT a Coordinate Frame at the CM
The quantities , , , , , and are called mass products of inertia and they can be positive, negative, or zero, and are given by,
They are a measure of the imbalance in the mass distribution.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 28: Inertia Tensor – WRT a Coordinate Frame at the CM
The angular momentum with respect to the center of mass G can be expressed in a matrix form as
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 29: Inertia Tensor – WRT an Arbitrary Coordinate Frame
For a rigid body that is free to move in a 3D space there are infinite possible rotation axes
The intertie tensor characterizes the mass distribution of the rigid body with respect to a specific coordinate system
The intertie Tensor relative to frame {A} is express as a matrix
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 30: Inertia Tensor
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 31: Tensor of Inertia – Example
This set of six independent quantities for a given body, depend on the position and orientation of the frame in which they are defined
We are free to choose the orientation of the reference frame. It is possible to cause the product of inertia to be zero
The axes of the reference frame when so aligned are called the principle axes and the corresponding mass moments are called the principle moments of intertie
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 32: Tensor of Inertia – Example
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 33: Tensor of Inertia – Example
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 34: Tensor of Inertia – Operations
Translations of the Inertia Tensor
Parallel Axis Theorem
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 35: Parallel Axis Theorem – 1D
The inertia tensor is a function of the position and orientation of the reference frame
Parallel Axis Theorem – How the inertia tensor changes under translation of the reference coordinate system
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
Frame {C} – is located at the CM
Frame {A} – an arbitrarily translated frame

## Slide 36: Parallel Axis Theorem – 3D
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
- Location of the CM (origin of C) relative to frame [A]

## Slide 37: Parallel Axis Theorem – 3D
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
Outer Product

## Slide 38: Tensor of Inertia – Example
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 39: Tensor of Inertia – Operations
Rotation of the Inertia Tensor
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 40: Rotation of the Inertia Tensor
Given:
  The inertia tensor of the a body expressed in frame A
  Frame B is rotated with respect to frame A
  Note: Both frames are stationary in space
Calculate
  The inertia tensor of the body expressed in frame B
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 41: Rotation of the Inertia Tensor
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
- angular velocity and momentum expressed in frame A
- angular velocity and momentum expressed in frame B

## Slide 42: Inertia Tensor 2/
The elements for relatively simple shapes can be solved from the equations describing the shape of the links and their density. However, most robot arms are far from simple shapes and as a result, these terms are simply measured in practice.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 43: Inertia Tensor 2/
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 44: Inertia Tensor 2/
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 45
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
Inertia Tensor – Robotic Links

## Slide 46: Inertia Tensor – Robotic Links
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 47: Inertia Tensor – Robotic Links
Body A
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 48: Inertia Tensor – Robotic Links
Body A
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
STEP 2 – Translate from frame A to the frame at the CoM of the link

## Slide 49: Inertia Tensor – Robotic Links
Body B
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
The frame of body B is aligned with the frame of the CM of the entire body

## Slide 50: Inertia Tensor – Robotic Links
Body C
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
STEP 1
See body A

## Slide 51: Inertia Tensor – Robotic Links
Body C
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
STEP 2 – Rotate about by

## Slide 52: Inertia Tensor – Robotic Links
Body C
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
STEP 3 – translate to the CM of the link
See body A

## Slide 53: Summary
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 54: Inertia Tensor – WRT a Coordinate Frame at the CM
The angular momentum with respect to the center of mass G can be expressed in a matrix form as
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 55: Inertia Tensor
The elements for relatively simple shapes can be solved from the equations describing the shape of the links and their density. However, most robot arms are far from simple shapes and as a result, these terms are simply measured in practice.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 56: Parallel Axis Theorem – 3D
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA
- Location of the CM (origin of C) relative to frame [A]

## Slide 57: Rotation of the Inertia Tensor
Instructor: Jacob Rosen
Advanced Robotic - MAE 263 - Department of Mechanical & Aerospace Engineering - UCLA