## Slide 1: Manipulator Dynamics 4
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 2: Lagrange Method
Introduction
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 3: Lagrangian Formulation of Manipulator Dynamics - Summary
1. Define a set of generalized coordinates for i=1,2,3…N.
These coordinates can be chosen arbitrarily as long as they provide a set of independent variables that map the system in a 1-to-1 manner. The usual variable set for serial manipulators is:
2. Define a set of generalized velocities for i=1,2,3…N
3. Define a set of generalized forces (and moments) for i=1,2,3…N
The generalized forces must satisfy
where is a small change in the generalized coordinate and is the work done corresponding to that small change, is the joint torque vector generated by the actuators, is the Jacobian matrix transposed, is the vector of the external forces and torques applied on the end effector, and is the friction torque vector generated at the joints
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 4: Langrangian Formulation of Manipulator Dynamics 2/
4. Write the equations describing the kinetic and potential energies as functions of the generalized coordinates as well as the resulting Lagrangian.
Let KE denote the expression describing the kinetic energy. Where
Let PE denote the expression describing the potential energy, where
Let L denote the Lagrangian given by:
L = KE - PE
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 5: Langrangian Formulation of Manipulator Dynamics 3/
5. The equations of motion are given by
or, more practically, by
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
( - )
0

## Slide 6: Gravity Effects - Langrangian Formulation
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 7: Manipulators – Non Linear Control Problem
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 8: Manipulators – Non Linear Control Problem
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 9: Lagrange Method
General Approach – Formal Derivation
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 10: Lagrangian Formulation of Manipulator Dynamics
Lagrangian function- The difference between kinetic and potential energy of a mechanical system:
Where:
  - Lagrangian
  – kinetic energy of a mechanical system
  – Potential energy of a mechanical system
The kinetic energy is function of the position and velocity of the link
The potential energy is a function of the position of the link
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 11: Lagrangian Formulation of Manipulator Dynamics
Lagrange’s equation of motion is
Where:
  - vector of generalized coordinates
  – vector of generalized forces
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 12: Lagrangian Formulation of Manipulator Dynamics
Kinetic Energy
Where:
is the inertia matrix of link i about its CM and expressed in the base frame (Frame 0)
is the inertia matrix of link i about its CM and expressed in the link frame
is the linear velocity of the CM of link i expressed in the base frame (Frame 0)
is the angular velocity of the CM of link i expressed in the base frame (Frame 0)
Note – The kinetic equation of each individual link is expressed with respect to base frame (Frame 0). The implication is that the velocities and the tensor of inertia should use the reference frame as frame 0
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 13: Lagrangian Formulation of Manipulator Dynamics
Kinetic Energy – Tensor of Inertia (Expressed in the Base Frame)
Rotating the moment of inertia of the link expressed in the i’th coordinate CM to the base frame
Where:
is the inertia matrix of link i about its CM and expressed in the base frame
is the inertia matrix of link i about its CM and expressed in the link frame
Note:
  - Time Invariant
  - Depends on to the robot arm posture because it is expressed in the base frame and the orientation of the link i with respect to the base is a function of joint variables
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 14: Lagrangian Formulation of Manipulator Dynamics
Kinetic Energy – Linear & Angular Velocity (Expressed in the Base Frame)
Methods for expressing the velocity of the CM at the base frame (Frame 0) ,
  Method 1: Recursive method
  Method 2: Partial Jacobian (Instantaneous screw motion) – Developed for each link as opposed to the previously defined Jacobian
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
[] = []

## Slide 15: Lagrangian Formulation of Manipulator Dynamics
  Partial Jacobian (Example)
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
[] = [] =
[] = [] =
[] = [] =

## Slide 16: Lagrangian Formulation of Manipulator Dynamics
  Partial Jacobian (Example) – Notes (Observations)
    Vectors Expressed in the Base Frame - The vectors placed in the partial Jacobian matrixes are expressed in the base frame (Frame 0)
      In the position vector is expressed with respect to frame 0
      In The joint rotation axis is expressed with respect to frame 0
    Population of Vectors - The columns partial Jacobian [] are populate with values for and columns for which are populated with zero
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
[] = []

## Slide 17: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Since the motion of link i depends only on the joints 1 through i the two vectors in the matrix are set to zero for j>i
=

## Slide 18: Lagrangian Formulation of Manipulator Dynamics
  Partial Jacobian – Generalized Interpretation
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 19: Lagrangian Formulation of Manipulator Dynamics
  Partial Jacobian – Generalized Interpretation
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 20: Lagrangian Formulation of Manipulator Dynamics
  Partial Jacobian – Generalized Interpretation
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 21: Lagrangian Formulation of Manipulator Dynamics
- The link Jacobian matrix - A 6xN matrix that maps the instantaneous joint rates into the instantaneous velocity at the center of mass
- Two 3xN submatrices of
- Position vector defined from the origin of the J joint frame to the CM of link i
, - the j’th column vector of respectivly
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
=
[] = []

## Slide 22: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Rewriting the Kinetic Energy
M

## Slide 23: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Define a nxn manipulator inertia matrix as
The total kinetic energy of a robot arm can be expressed in terms of the manipulator inertia matrix and the vector of joint rates
M is configuration dependent because and are configuration dependent as well
Properties of the mass matrix M:
  Symmetric
  Positive Definite
The quadratic form of the equation indicates that the kinetic energy is always positive unless the system is at rest

## Slide 24: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Potential Energy
  Potential energy stores in a link is defined as the amount of work required to raise the center of mass of link from the horizontal reference plane to its present position under the influence of gravity
  With reference to the inertial frame (frame 0), the work required to displace link to position is given by

## Slide 25: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Generalized Forces
  Grivation forces
  Inertial forces
  All the rest
All the forces acting on a robot arm that consistent with the mechanical constraints
The vector of generalized forces is defined by the principle of virtual work as
Actuators -> Force/Torque at the joint
External Forces/Moment -> End Effector

## Slide 26: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Where
  - n dimensional vector of joint torques generated by the actuators
  - n dimensional vector of joint displacement generated at the joint
  – six dimensional vector of resultant force and moments exerted at the end effector
  – six dimensional virtual displacement vector of the end effector
  – virtual work

## Slide 27: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Substituting
We have
Joint Torque
External Forces

## Slide 28: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Joint Frictions
  Highly Non-linear
  Grease/oil lubricated bearing – Types of frictions
    Static friction
    Boundary lubrication
    Partial fluid lubrication
    Full fluid lubrication
  Full fluid lubrication
  – The frictional torques or forces in the joints. The minus sign indicates that the direction of the frictional torque or forces is always opposite to the joint velocity.

## Slide 29: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Total Generalized forces including the joint’s fluid lubrication resulted in

## Slide 30: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
General Form of Dynamical Equations
Expand the term for the kinetic energy into a sum of scalars
- The (i,j) element of the manipulator inertia matrix M

## Slide 31: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Take partial derivative of with respect to
Note that the potential energy does not depend on
Taking the derivative of with respect to time

## Slide 32: Lagrangian Formulation of Manipulator Dynamics
Taking the partial derivative
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
The ith column vector of the link Jacobian sub matrix

## Slide 33: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Substitute all the equation into the Lagrange Equation

## Slide 34: Lagrangian Formulation of Manipulator Dynamics
Substitute all the equation into the Lagrange Equation
Where
  - is the Inertia
  - is the Coriolis and centrifugal force
  - is the gravitational effects
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 35: Lagrange Method
2R - Example
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 36: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Example: 2DOF robot
  Note: The link coordinate axes are aligned with the principal axes at each link

## Slide 37: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(a) Link Inertia Matrix: Assume that the length of the link is much longer than the radius of the link L>>r
Assume L>>r

## Slide 38: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
= =

## Slide 39: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(b) Link Jacobian Matrix:

## Slide 40: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(b) Link Jacobian Matrix:
  Position of the CM:

## Slide 41: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(b) Link Jacobian Matrix:
  Position of the CM:
=

## Slide 42: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
=

## Slide 43: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 44: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 45: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 46: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 47: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(c) Manipulator Inertia Matrix:

## Slide 48: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 49: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 50: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 51: Lagangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 52: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 53: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(d) Velocity Coupling Vector:
(- 1/2 )

## Slide 54: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(e) Gravitational Vector

## Slide 55: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
(e) Gravitational Vector

## Slide 56: Lagrangian Formulation of Manipulator Dynamics
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
+ +

## Slide 57: Lagrange Method
Summary
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 58: Lagrangian Formulation of Manipulator Dynamics – Summary
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Step 1: Define a set of generalized coordinates for i=1,2,3…N. The usual variable set for serial manipulators is:
Step 2: Define a set of generalized velocities for i=1,2,3…N
Step 3: Define a set of generalized forces (and moments)
Step 4: Define the new tensor of inertia at the base frame (frame 0) by transforming the tensor of inertia of all the links form the links’ coordinate systems to the base coordinate system for i=1,2,3…N

## Slide 59: Lagrangian Formulation of Manipulator Dynamics – Summary
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Step 5: Define the frame positions of the links with respect to the base frame as well as the positions of of the center of mass in their own coordinate systems for i=1,2,3…N. manipulators is:
Step 6: Define the element in the partial Jacobean matrix for i=1,2,3…N
Step 7: Define the inertia matrix

## Slide 60: Lagrangian Formulation of Manipulator Dynamics – Summary
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Step 8: Calculate the velocity vector for i=1,2,3…N. as:

## Slide 61: Lagrangian Formulation of Manipulator Dynamics – Summary
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Step 9: Calculate the gravity vector for i=1,2,3…N. as:
Note that the gravity is defined as

## Slide 62: Lagrangian Formulation of Manipulator Dynamics – Summary
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA
Step 10: Define the equation of motion for i=1,2,3…N. as:

## Slide 63: Equations of Motion in Various Spaces
Joint Space versus Task Space
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 64: Dynamic Equations - State Space Equation
It is often convenient to express the dynamic equations of a manipulator in a single equation
where
- Mass matrix (includes inertia terms) - nxn Matrix
- Centrifugal (square of joint velocity) and Coriolis (product of two different
joint velocities) terms - nx1 Vector
- gravitational terms - nx1 Vector.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 65: Dynamic Equations - Configuration Space Equation
By rewriting the velocity dependent term in a different form, we can write the dynamic equations as
where
- Centrifugal coefficients(square of joint velocity)
- Coriolis coefficients (product of two different joint velocities)
We may refer to this formulation as the configuration space equation or the joint space
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 66: Dynamic Equations - Cartesian State Space Equation
It can sometimes be desirable to have a relationship between the end effector’s Cartesian accelerations and the joint torques.
Beginning from the Configuration Space equation
we can substitute the joint moments using our definition of the Jacobian matrix:
By differentiation, we find
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA

## Slide 67: Dynamic Equations - Cartesian State Space Equation
Solving for joint acceleration gives
Substitution yields
Where
This equation relates the forces and moments at the end effector to the Cartesian accelerations of the end effector and the manipulator joint positions and velocities.
Instructor: Jacob Rosen
Advanced Robotic - MAE 263D - Department of Mechanical & Aerospace Engineering - UCLA